## Slide 1: Single vs Dual Spur Gear for Handwheel Position Sensor
09AP14

## Slide 2: SGMW 200 Digital Position Sensor
Enhancements for Next Build (Week of April 14)
  Allegro BC Chip – Significant Enhancement (Refer below)
  Software update (dll & software release) …. Averaging
  Probe Housing Shift of 1.0 mm (Location of Hall to Magnet)
  Patent Search (2 Spur Gear) ---- Completed with no evident issues
In the chart below, the first ~190 points are from the sorting that was done in China (BB'). The first box are from the post DV testing (BB'). The second box is from the BC 1332s with the Max Baermann higher strength magnets (~50% increase) on the lower rotor assemblies. The third box is from the BC 1332s with the standard production lower rotor magnets.

## Slide 3
C1XX Probe Housing Assembly Issue – Executive Summary
Problem Definition
  Signal of the ring magnet in the probe housing assembly yields excessive error not suitable for the Nexteer manufacturing system (High FTQ)
Immediate Containment/Certification - IVER
  Probe Housing 100% certified at component level
  System level function test (Sensor Test, EOL)
Root Cause
  Signal Strength of ring magnet not adequate half way between north and south poles
Past Improvement Development Activities
  Evaluated hall sensor enhancements
  Evaluated stronger ring magnets
  4 pole magnets
  2 levels of algorithm improvements
  Multiple other concepts pursued
Robust Permanent Corrective Action
  Replace the ring magnet function with a second spur gear which provides much improved accuracy
  Layout change (No change to schematic)
  Corresponding software algorithm
Verification
  4 weeks - Mechanical Validation (See Slide # 7)
  Electrical Validation (3172 Thermal Shock Testing for Probe Housing Asm – K2XX Profile)
  EMC – Include in next round of EMC system testing

## Slide 4: Dual Spur Gear
4
Additional Spur Gear to be added
11 Tooth
10 Tooth
Single Spur Gear
Lower rotor Magnet
to be removed

## Slide 5: SENSOR – Position – Digital
Ring Magnet
N
Flux
S
N
S
In the digital system there is a single hall probe which is measuring the direction of the signal. The specified minimum magnitude of this signal is 100 G. With the ring magnet design, this signal strength was found to drop off significantly when the sensor is half way between the north and south poles. Weaker signal strength results in increased error.
Signal Strength concern
Chart: Flux Collector Test

## Slide 6: Digital Spur Gear Sensor
N
S
Magnet
Hall Probe
Each spur gear contains a single puck magnet. The hall probe is located directly above puck magnet. This provides a consistent magnetic magnitude of roughly 250 gauss, regardless of magnet position.

## Slide 7: Dual Spur Gear Timing / Validation
C1xx design: complete
Initial Samples: 20JN14
Mechanical Validation: (4 weeks)
  4 parts on component level test (pinion shafts and probe housing asm)
      2 parts rotated to represent bottoming cycles
      2 parts rotated to represent target life cycles
  2 parts on random vibration
Cost request in process (47107)
  Expectation is for small saving or same cost for Dual Spur design
    Elimination of ring magnet: --
    Addition of 2nd gear: ++
    Modification to PH: 0
    Modification to retainer: +
    Modification to PCB: -

## Slide 8: PCB layout change
Single Spur Gear
Dual Spur Gear

## Slide 9: Ring Magnet vs Spur Gear Accuracy
The purple line below shows the typical error for a ring magnet sensor
The green line below shows the typical error for a spur gear sensor (puck magnet)

## Slide 10: Position Algorithm Single Spur vs Dual gear
Chart: Steering Wheel Position (deg)
Chart: Steering Wheel Position (deg)
Step=ColSen-10Tooth/2.2
Step=10Tooth-11Tooth*11/10