## Slide 1: Disruptive Cost - LO CEPS (Baseline: CR3005897 for Fiat 319/332) Stage I: CR3007570 (on going) Stage II: Feasibility and saving review
2016.05.16

## Slide 2: Product Content Description – stage I (tangible initiatives)
Fiat 319 design, 30 Nm & 56 Nm assist
Only EA 4, only brushless
Rake only column with energy absorb
AM & Worm:
CR3005897 baseline:
Fix worm
Solid coupling
Zoning, no eccentric
Mounting hole machining in house
Friction spec relief
No paining
New initiatives:
31:1 gear ratio
2 lead worm
24 OD worm bearing
Fast whirling + Fast grind worm process
Shaft Assembly & Sensor:
CR3005897 baseline:
Stamp stator lower rotor
No knurl on upper shaft to upper rotor interface
Remove knurling for gear interface
New initiatives:
Axial stack sensor upper rotor
Change spline to knurl on lower shaft interface to lower rotor
No degaussing process
2 stop teeth
No sticky grease
T-bar simultaneous press
MPP and EE:
CR3005897 baseline:
EA4
Baseline flash 1 Meg
2.9mOhm D2PAK
Current mode
Turns counter
Digital torque sensor soldered to CCA
Hall calibration table processing time
PHA: Selective solder changed to Wave Solder
PHA: FR4
TC: A1331 changed to A1337
New initiatives:
Motor with steel can
Smaller motor for 31:1
Schematic optimized
Eliminate components for "back EMF monitoring"
Column:
CR3005897 baseline:
Single piece rake bracket
14 teeth shaft
Capsule no coating
Common inner compression bracket
Share VSS laser welding equipment
New initiatives:
Press fit w/o EA strap
Column make in house with parts P2P
Tangible Initiatives:
With DEV validation
With similar application
With supplier input
With benchmark competitor
With CAE evidence

## Slide 3: Cost down initiatives– stage II
White items are followed by Disruptive PDT
Highlighted items are not followed in PDT.

## Slide 4: Cost down initiatives– stage II
Need to identify a way to follow these effectively to
  Clarify direction, priority
  Guidance estimate saving for each product family
  Resource/ownership
  Timing plan
  Communicate progress/result to disruptive task force
These items can classified in 5 groups:
AM (yellow)
Motor (blue)
PCB (brown)
EE (pink)
Grey Box (grey)

## Slide 5
Back up slides of Stage I design details

## Slide 6: Shaft-Sensor Rotor Interface change and Two-Tooth Stop Teeth - Upper Assist Shaft
38222055
38219969
22.76 mm
27.5 mm
Stop teeth profile
Stop teeth profile
Knurling
No knurling

## Slide 7
38222053
38004142
26 mm
Stop teeth profile
Stop teeth profile
28.5 mm
24 tooth spline
26 mm
Class 3 straight knurl
Shaft-Sensor Rotor Interface change and Two-Tooth Stop Teeth (cont.)
- Lower Assist Shaft

## Slide 8
Press lower rotor to shoulder
Press lower rotor to gear hub
Press lower rotor BEFORE t-bar press
26.2mm
25.8mm
Shaft-Sensor Rotor Interface change and Two-Tooth Stop Teeth (cont.)
- Assist shaft assembly

## Slide 9
38221638
Diameter enlarged with
same magnets
27.5 mm
56.74 mm
SG207143
Baseline axial Upper rotor
52 mm
22.76 mm
Axial Sensor application - Upper Rotor

## Slide 10
38221399
Diameter enlarged for Two-tooth Stop Teeth design
38219359
Baseline axial Lower rotor
Torque only design
19.8 mm
55.3 mm OD
24 tooth spline 23.185mm minor dia
13.8 mm
57.14 mm OD
No spline
26mm dia
Axial Sensor application (cont.) - Lower Rotor

## Slide 11
Axial Sensor application (cont.) - Assist Housing machined

## Slide 12
Axial Sensor application (cont.) - Sensor Cover

## Slide 13: Reference CAD model of SG212037 (the latest design w/ 24mm bearing)

## Slide 14: Fiat 319 split vs press-press upper jacket
Baseline – split upper jacket
New – press press upper jacket
Remove split from upper jacket
Add 8 pad protrusions to upper jacket
Change from two piece compression bracket to single piece
Change from laser weld to MIG weld for compression bracket to upper jacket weld
Change from slip fit to press fit between upper & lower jackets.

## Slide 15: Fiat 319 remove E/A straps
Remove E/A straps & retainers
Remove holes for strap retainer from rake bracket