## Slide 1: Cut and Coin – BMW
Note – No mid-plane tooth laps
Cut Form
Finished Teeth
Tonnage & Fill
Cut Form

## Slide 2: Variable Ratio Rack Development
Rack Technology team now headed by Bill Anders
  Completed Die set for forming operation
  Completed forming by cut and coin of 9 tooth T1 rack
Shifting focus to developing BMW rack by cut and coin

## Slide 3: Variable Ratio Rack by cut and coin
Process used to manufacture Variable Ratio Racks
Manufacture straight ratio racks by milling
  Use hydraulic press to coin the teeth into the VR geometry
    Not the same as G-Car - entire tooth mesh is coined to provide seamless transitions
  Suitable for applications such as BMW.
  Capital investment limited to pressing operation to coin teeth
    Remaining processing remains same as straight ration production