## Slide 1: SGMW 200 Digital Position Sensor
Enhancements for Next Build (Week of April 14)
  Allegro BC Chip – Significant Enhancement (Refer below)
  Software update (dll & software release) …. Averaging
  Probe Housing Shift of 1.0 mm (Location of Hall to Magnet)
100 samples for the SGMW 200 Handwheel Position sensor using the new plastic housings along with the new Allegro chips were measured in Suzhou this week and demonstrated a 2x improvement in the Gauss level as expected. The new software updates (dll & software release) has also been implemented which will reduce our error by 50 % for the builds that will take place later this week.
A higher than expected vernier error (spur gear to handwheel sensor) was seen on the SGMW 200 Handwheel position sensor during the build last week. Additional tuning of the software associated with the calibration dll is taking place to minimize the issue.