## Slide 1: Electromagnetic Projects to be Included in Technology Road Map

## Slide 2: 1. Reduce Motor Friction
Description
  REPS gear w/reduced friction for certain premium customers (e.g. Ford CD6)
Motivation
  To be competitive with other competitions offering low friction gear
Deliverables
  Identify all components of friction budget/allocation
  Reduce motor hysteresis by design /material selection
  Si steel vs. other higher grade materials (Ni-Iron, Co-Iron etc.)?
Timing
  Concept development and analysis / Selection : April 2015
  Concept design and build complete : August 2015
  Other exotic material selection decision : October 2015
Team Members/Customers
  Alejandro, Rakib, Steve Collier-Hallman
Motivation (6)

## Slide 3: 3. Segments / Ring Magnets?
Description
  Gain better control on cogging and harmonics and reduce part to part variation . Learning cost trade offs
  Motivation
  Smaller motor using arc segments with multiple pieces per pole become challenging for making the magnets as well as placing on the rotor. Ring magnet solution can eliminate that challenge.
Deliverables
  Cost study with magnet supplier-- Target program is BMW-30.5mm
  Complete analysis for a 9/6 motor replacing 2-step skewed design by a ring magnet
  Build motors based on the analysis for 20~30 mm long stack lengths (Say, FIASA)
  Timing
  Analysis : June 2015
  Concept design and build complete: September 2015
  Testing complete : November 2015
  Further tuning of the design / decision : December 2015
Team Members/Customers
  Subhra Paul, Rakib?
Motivation (4)

## Slide 4: 4. Skewed Stator-Alternate to Ring Magnet / Skewed Arc
Description
  Gain better control on cogging and harmonics and reduce part to part variation . Learning cost trade offs
  Motivation
  Smaller motor using arc segments with multiple pieces per pole become challenging for making the magnets as well as placing on the rotor. To overcome the challenges in rotor skew when comes to a smaller magnet length skewed stator is one form of solution
Deliverables
  Complete study with 9/6 motor w/ skewed stator
  Build motors around 30~40 mm long stack lengths (Lamination from LH and wound by ATS), Target program is BMW—30.5mm
  Timing
  Ordering parts : June 2015
  Concept design and build complete: September 2015
  Testing complete : November 2015
Team Members/Customers
  Robert Long, Sai, Alejandro
Motivation (4)

## Slide 5: 6. 12/10 Motor
Description
  Optimize motor design by selecting motor topology
Motivation
  Need to relook at this design as it is the highest torque density motor
  Mechanical/structural work needed to address NVH tied to this motor topology?
Deliverables
  Do a cost model of the current Honda Fit system first
  Complete validation leveraging the 12-slot stator parts from 12/8 builds for a 12/10 motor
  Idea of potted stator or any other concept to improve structural stiffness
  Complete sizing comparison with 12/8 , 9/6 and 27/6 motor
Timing
  Analysis : August 2015
  Concept design and build complete: October 2015
  Testing complete : December 2015
Team Members/Customers
  Rakib, Subhra, Rakesh, Robert
Motivation (6.5)

## Slide 6: 11. Needle Winding w/Multiple WIH
Description
  With more WIH can enhance the capability of needle winding design to compete with shed / segment winding
Motivation
  Making needle winding more of a scalable design
Deliverables
  Complete comparative study on the BMW X3, X5 system
  Come up with termination design scheme for more than 2 WIH
  Proof of concept with prototype build (say, 12/8 motor)
Timing
  Comparative study : June 2015
  Concept of termination scheme : September 2015
  Prototyping : November 2015
  Testing & design decision : December 2015
Team Members/Customers
  B. Williams, Chris
Motivation (4)

## Slide 7: 13. Automotive Electric Water Pump (EWP)
Description
  Improve fuel efficiency by electric motor used for the water pump
Motivation
  Initial assessment completed in the technology roadmap review meeting and found worth to pursue
  Improve Engine management, pump efficiency
  Improves Packaging (Compact in size).
  Emission Improvement and reliability.
  Accessories minimization
Deliverables
  Performance data of Non Electric water pump
  Design and Develop proto with minimum cost and improved performance of EWP
Timing
  Analysis : June 2015
  Further tuning of the design / decision : December 2015
Team Members/Customers
  Subhra, AL Armitage, Steve Collier-Hallman, Sai Saagar
Motivation (5)

## Slide 8: 14. Electric Brake Booster
Description
  Electric motor as brake boosting operation
Motivation
  Initial assessment completed in the technology roadmap review meeting and found worth to pursue
Deliverables
  Based on requirements complete motor sizing
Timing
Team Members/Customers
  Brian Magnus, Sai, ??
Motivation (5)

## Slide 9: 17. Next Generation Position Sensor
Description
  Develop position sensor for higher accuracy/resolution
Motivation
  To improve position accuracy
  To achieve better resolution as motor designs with higher poles evolved
Deliverables
  Position sensor alternatives- a broad search
  Analog/Digital/GMR/TMR ???
  Sense magnet design / sensing technology selection
Timing
  Analysis and design by Q4 2014
  Procure components and build prototype by Q2 2015
  Test and fine tune design end of Q2
Team Members/Customers
  Ken Sabol, Steve CH, Paul Fisher,??,
Motivation (7)