## Slide 1: REPS Ratio
June 2014

## Slide 2: Ratio Summary

## Slide 3: Overall Ratio
History
  Systems and Motor engineering desired the highest possible ratios
  Had jump-over internal ball return
  Didn’t have toothed belts
Historic Constraints
  Packaging wasn’t a huge constraint
  R&P grease didn’t perform well in cold in ballnut/ballscrew
  Ballscrew development is difficult. Not just a question of scaling.
  Inertia
  Motor speed

## Slide 4: Drive Pulley
History
  Original design dictated by overall ratio optimization
Constraints
  30 tooth is smallest we want for
    Belt radius bending/fatigue concerns
    PM pulley wall thickness over a 10 mm motor shaft (12 mm requires larger pulley)
  35 tooth is smallest before needing a tensioner
Current Design
  Tooth design and width dictated by belt design

## Slide 5: Driven Pulley
History
  Steel
  Original design dictated by package within bearing bore with bearings that could react the loading
Constraints
  Package
    Large constrained by size in bore
    Small constrained by ballnut plus return guide OD
Current Design
  Plastic
  124 teeth / ballnut rev
  Tooth design and width dictated by belt design

## Slide 6: Rack Ball Screw
History
  5 mm and 6 mm leads were tried for more ratio
    Very small balls
      Noisy, poor durability, poor backdrive, poor cold performance
  8 mm lead was originally designed for a 25 mm rack
  Kinefac rollers didn’t perform well
Constraints
  5 degree lead angle minimum rule of thumb
    For backdriveability. Came from someone at Thompson Ball Screw.
  Manufacturing wants a common lead for all Rack Diameters
    Dies are same for 28 mm and 31 mm (Also will be for 26 mm)
Current Design
  8 mm lead
  Rolled ball track (Profiroll) is used for better NVH performance
    Alternatively, grinding creates white noise, however is better for efficiency due to less lead related errors.

## Slide 7: Ball Nut
History
  Jump-over internal bank return
Constraints
  Minimum lead is constrained by return geometry. Smaller lead would interfere with adjacent track wall thickness at return port.
  Lead < 8mm will require a different ball return strategy.
Current Design
  External return is very good for NVH and cost
  Smaller package return (OD) under development to mitigate pulley roundness issues but could help driven pulley min size constraint if that were ever desired

## Slide 8: Belt
History
  Grooved Poly V-belt
  Gates 2 mm pitch, 5 degree helix
    Optimal for durability (force into flange) and NVH
Constraints
  Durability / bending. Minimum of 30 tooth drive.
  Consistent angle for tensioning.
  Minimum width (UP375 = 25 mm wide)
Current Design
  Gates Standard Tooth
  Gates Deep Tooth
    2 mm pitch, 5 degree helix, ~.130 mm deeper tooth
  Dayco Standard Tooth
    2 mm pitch, 6 degree helix, ~.165 mm deeper tooth

## Slide 9: Summary
Mechanical Trade-offs for a smaller motor
Assist Ratio
Belt Ratio
1 / Lead
.125
Numerically Higher
Higher:
Motor Speed
Inertia
Increased Backdrive
New ball return design
Proliferate BS Manufacturing
Larger Package
Tensioner

## Slide 10: Reference
Nexteer Ball Circuit Designs