## Slide 1: SE43 – Limp Home Motor Phase Current Sensor
Description
  Eliminate Loss of Assist for diagnostic failures of a motor phase current sensor.
  Operate system in feedforward torque control mode (voltage mode) during the limp home event.
Motivation (Score: 6.5)
  Some of our customers are requiring this capability today
  More are expected to require this soon
Deliverables
  System, subsystem, and FDD requirements for function.
  Prototype software suitable for customer use on test track.
  Production SW FDD’s.
  Test Plans
Timing
  FDD requirements for PSR complete by May 15, 2014
    PSR Request submitted May 27, 2014
  PSR Software to customer by end of July 2014
    Demo was moved to September 2014
  Ford S550, March 2016 SOP
Team Members/Customers
  Systems - MC&S: Julie Kleinau, Prerit Pramod, Siddharth Ballal
  Systems - Functional Safety: Kathy Pattok, Scott Weiss, Mark Norman
  Customer – Ford S550/P552 PDT

## Slide 2: SE43 – Limp Home Motor Phase Current Sensor
Status
  System Level Requirements Drafted
  Preliminary FDD Models Completed
    Interface for Assist Torque Gains and Ramps implemented in Controlled Disable Shutdown.
    Production interface for ramps and damping will be common with other Loss of Assist mitigation functions – interface is under development by safety group.
  Customer Accessible Fault Injection Point implemented to induce fault on the fly.
  PSR 613C provided to customer.
  Nexteer Saginaw test track testing completed over wide range of fault levels and assist ramp configurations.
  Multiple fault levels tested for current offset error to evaluate transition from current mode to voltage mode
  Customer was provided standard ramp down of assist gain multiplier - some temporary damping provided during the transition.)
Challenges
  None significant.
Next Steps
  Resolve secondary F1 diagnostic trip issue (related to CLOA design or not? Corrective action?) – October 15, 2014.
  Q3/Q4 Timeframe – rework interface to be compatible with new current loop structure being rolled out this summer to all programs (will interface differently than on the Ford S550/P552 current loop design). – target completion November 2014.