## Slide 1: CCM-81: Short T-bar Profile Grind (Gen 4)
Gen 4
Description
  Shorter bar, shallower holes, shorter stop tooth travel, increased hardness, larger press interference range, higher press load tolerance & lower hysteresis
Motivation : 2.0
Deliverables
  Lower hysteresis and cost
  Press & fatigue robustness
  MQ, PV Build success
    Capable to +/- 1° stop tooth balance
  Eliminate the need for lubrication
Timing
  Print and DSS update: 26JN15
Team Members/Customers
  Team names: Dan Diffin
  Customers: Applications Teams
Last updated: 01JA15
Gen 3

## Slide 2
Status Update:
Lower cost than Gen 3
  Less material, shallower holes
  Profile grind is faster with less wheel breakdown due to no bullet nose
    However cost request show the cost to be similar to Gen 3
Hysteresis below 0.2Nm
Robust to press & short stop tooth fatigue
  Higher allowed press load: Lubricant not needed but may still be preferred to reduce load variation
  4 parts completed 75 lives of fatigue without torque drop at Gen 3 stop tooth travel
Challenges:
Drill only holes preferred but internal and external sources want to ream
Need to understand ream step affects on t-bar press curve and stopping position.
Next Actions:
Print updates with new hardness notes and minor updates
Ream step press study
Last updated: 08JN15
CCM-81: Short T-bar Profile Grind (Gen 4)