## Slide 1: CCM-85: Skewed Worm Axis for SPEPS – 15° Intersect Angle
Description
  Develop and characterize a 15° skewed worm gear set
Motivation : XX
Deliverables
  Assist mech durability
  Acceptable NVH performance
  Backdrive performance
  Efficiency
Timing
  Assist mech durability – Ongoing
    Running parts with conditioning cycles
    Running parts with varying run-in cycles (changing load and speed)
Team Members/Customers
  Team names: Jeff Beyerlien / Adam Lee
  Customers:
Last updated: 23FE16

## Slide 2: CCM-85: Skewed Worm Axis for SPEPS – 15° Intersect Angle
Status Update:
AM bottoming tests ongoing
  At current load of 74Nm, durability is not a concern
  Parts have develop lash/low backdrive very early
Zoning
  High FLV/TPV at backdrive speeds of 30RPM.
    Problem does not exist at 5RPM
    Removing/uncompressing isolators improves the backdrive plot.
Next Actions:
NVH
  Need to do a rattle study in vehicle to determine acceptable level of backdrive after 1 life.
  Put high FLV/TPV parts in car to determine acceptable level
Challenges:
Assist mech stand availability
Poor AM bottoming performance
Part/vehicle availability for NVH
Last updated: 23FE16