## Slide 1: CCM-85: High Output (above 90Nm) CEPS
Description
  Validate a 90Nm+ gear design for CEPS
Motivation : 4.0
Deliverables
  Assist mech durability
  Acceptable NVH performance
Timing
  Assist mech durability – marginal to 100Nm
  Bench noise testing – 6-8 weeks
    AM bottoming w/ pre and post rotation noise and FDR
Team Members/Customers
  Team names: Jeff Beyerlien / Adam Lee
  Customers: James Burghardt / Nick Trewhella
Last updated: 03AU15

## Slide 2
Status Update:
Parts tested at 90Nm
  Stopped after 7+ lives
Parts tested at 95Nm
  1 gear stopped at 5 lives
  1 gear failure at 4.5+ lives
  1 bearing failure at 2.4+ lives (may have been related to dummy motor)
Parts tested at 100Nm (100 Nm bottoming on every cycle and 540°EOT)
  3 gears run to failure – 2.75, 3.77 ,4.04 lives
  1 part stopped at 1 life (70°C ambient temperature during test)
  1 part Failed at 0.75 lives (70°C ambient temperature during test)
  1 part running (70°C ambient temperature during test) – 1 life
Test parts at 100 Nm with more realistic profile
  Need test stand
Test parts with larger gear OD
  1 part running
Challenges:
Need a firmly defined loading profile
Vehicle availability for NVH evaluations
Need motor capable of 100Nm+ of assist
Assist mech stand availability
Next Actions:
Define realistic load profile - 100Nm (Trewhella)
        Acquire larger motor/powerpack (Roller)
Perform bench noise testing (Beyerlein)
CCM-85: High Output (above 90Nm) CEPS
Last updated: 03AU15