## Slide 1: CCM-129: Stiffer Assist Path for Worm Shaft
Description
  Develop single isolated bearing worm axis design
Motivation : 14.0
Deliverables
  Find appropriate worm axis bearing configuration
  Coordinate BMPV demos
  Find rattle threshold (friction)
Timing
  ASAP
Team Members/Customers
  Team names: Brad Sundholm
  Customers: Application Teams
Last updated: 13AP16

## Slide 2
Status Update:
Assist Mech Bottoming Testing
  Damped vs Fixed vs SIB Worm Axis
  100Nm VSS test profile
  Track backdrive vs cycles and gear failure
PSA BMPV Demo
  System being built as a proof of concept for the PSA CMP program
  Two different SIB configurations and a fixed worm will be built
Increased Worm Travel SIB
  SIB high travel isolators (+/- 0.50mm)
Gamma SIB Demo
  Use for tuning and rattle threshold testing
Challenges:
Determining best configuration for worm axis bearings
Getting and modifying parts for BMPV demo
Next Actions:
Find proper worm axis bearing configuration to reduce rattle yet keep friction low
Obtain BMPV components / systems for modification and demo build
Build Gamma demo
Last updated: 13AP16
CCM-129: Stiffer Assist Path for Worm Shaft