## Slide 1: LoA – Estimates: Single Micro, Dual Inverter
Failure Rate Catalog | Mission Profile / Temperature | Base Design FIT | Added Components FIT
SN29500 | 55C | 145 FIT | 76 FIT
SN29500 | 69C | 213 FIT | 103 FIT
IEC 62380 | Passenger Compartment | 292 FIT | 176 FIT
IEC 62380 | Eng Comp | 427 FIT | 253 FIT
IEC 62380 | Ford CEPS Profile | 343 FIT | 199 FIT
IEC 62380 | Ford REPS Profile | 500 FIT | 294 FIT
Did not achieve 100 FIT, so develop dual micro proposal

## Slide 2: Additional FIT Rate Improvements…Beyond just dual inverter
In the Dual Inverter…Largest remaining contributors to LoA (IEC 62380 w/Ford REPS temperature):
  Microprocessor & CPU Clocking Circuit (~147 FIT)
    Micro’s raw failure rate = 172.5 FIT, ~69 FIT residual
  ECU Power Supply (~96 FIT)
    This number already includes as many improvements as practical including series capacitors to eliminate single point LoA. (Base failure rate = 220 FIT)
  Reverse Battery Protection Circuit (~23 FIT)
Next steps to achieve <100 FIT:
  Dual microprocessor with independent power supplies.
    Design can still include the use of the same battery supply voltage, battery filtering circuit, and reverse battery protection.
    Achieved 48 FIT with Ford REPS temperature profile

## Slide 3: Mechanization
LoA FIT: 48 FIT
  Ford REPS temperature
Remaining LoA FIT sources
  Shared components:
    Power Filters
    Reverse Battery Protection
Not included
  Vehicle power supply