## Slide 1: N. Champetier visit – Saginaw Technical roadmap & Innovation
30 October 2015
Saginaw, Michigan

## Slide 2: N. Champetier visit – Saginaw Technical roadmap & Innovation Content
Our approach to innovation
EPS building block roadmap
ADAS & Autonomous driving roadmap
None-Steering automotive projects

## Slide 3: N. Champetier visit – Saginaw Technical roadmap & Innovation Content
Our approach to innovation
EPS building block roadmap
ADAS & Autonomous driving roadmap
None-Steering automotive projects

## Slide 4: Our approach to innovation Value-Managed Technology
Develop technologies to meet future customers and business needs
Ensure technology for future market growth and strength
All EPS Engineering projects managed and tracked in Technology Roadmap
Weekly meetings with cross functional group
Projects assessed and prioritized based on overall value
High risk projects reviewed weekly, others based upon scheduled cadence
Responsive development process
Project requirements defined for each project – exit criteria and timing

## Slide 5: Our approach to innovation Value-Managed Technology
Value rating scale considers trade offs between attributes
120 Total Active Projects
13.5% Value Improvement average over current state
Value Attributes
Cost
Mass
Packaging
Performance
Quality
Value Stream/Risk Reduction
Developmental Efficiency
Growth Opportunity

## Slide 6: Our approach to innovation Leverage our core competencies
What new products could we develop from these?
Mechanical Integration
Power Electronics
Software
Algorithms
Motor Design
Sensor Design
Safety Critical Product Creation from requirements
Systems Engineering
Closed Loop Servo Control
Ability to Industrialize

## Slide 7: Our approach to innovation Technology Development and Work Flow
Pursuit
Power Pack
Future
Core
Applications
Systems and Electrical
Zuraski
Maleki
Sizelove
Chandy (previous role)
Bright
Roller
Arnold
Singh
Work is distributed (not all projects start in FE)

## Slide 8: Our approach to innovation Technology Development and Work Flow
Milestone 1
Milestone 0
Milestone 2
Milestone 3
Milestone 4
Milestone 5
Process
Proof of Concept
DEV
PV
Production
Review w/ Product Team
Risk Assessment
Big Bang Initiatives
Davis
Supporting Activities
Staff Linkage
New
Future
Zuraski
Core
Maleki, Sizelove
Current / CIP
Burns, Davis
Brush CIP Workshops
Huang
Red = Date Delayed
Yellow = Date at Risk
Green = Date on Track
No longer tracked by Tech Roadmap
In a Program at SOP
Ready to Use –
On the Shelf
Ready for Project Transfer
Product Team Review & Approval
Concept
Weekly Meetings to Review Status
DV
Validation in Process
Closed
Note: Initiatives may go into Tech Roadmap if further development is required or directly to ECR/CR/CRB
CIP Advanced Planning Roadmap/Overlay
Linkage to Program Timing, Bundled Validation Windows
and Target SOP Windows
Core – CAT 1
Application
Singh
Closeout & Transfer Review(s)

## Slide 9: Our approach to innovation Key Project Drivers
MARKET TRENDS
71 projects positively impact our growth opportunity
Project Examples
Automated Driving Trends – 3 projects
Advanced Steering Features – 13 projects
Enhanced Safety Systems – 12 Projects

## Slide 10: Our approach to innovation Key Project Drivers
PACKAGING
29 projects positively impact our packaging
Skewed worm axis
Overlapping A/M coupler
Radial Field MSB
Compact brush motor
Remote mounted controller
Remove isolation on worm axis
MASS
28 projects reduce system Mass
Plastic housing
Plastic pulleys
Hollow/Tubular racks
High ratio CEPS

## Slide 11: Our approach to innovation Key Project Drivers
COST IMPROVEMENTS
48 projects positively impact reducing our product cost
New Electrical Architecture
Support AutoSar 4 and ISO 26262
Plastic conversion of components
Synchronous reluctance motor
Power inverter optimization
Motor and Controller optimization

## Slide 12: N. Champetier visit – Saginaw Technical roadmap & Innovation Content
Our approach to innovation
EPS building block roadmap
ADAS & Autonomous driving roadmap
None-Steering automotive projects

## Slide 13: EPS building block roadmap Focus on SPEPS 2018 – 2022 timeframe
2019
2020
2021
>2022
Stiff worm shaft
Simplified stop teeth
Simplified lower rotor
EA4, CyberSec
Redundant MPP
Integrated Single Bearing BNA
Plastic driven pulley
Plastic drive pulley
Motor Rotor technology
High gear ratio
Optimized sensor
Push-in power connections
PHA using FR4 PCB

## Slide 14: N. Champetier visit – Saginaw Technical roadmap & Innovation Content
Our approach to innovation
EPS building block roadmap
ADAS & Autonomous driving roadmap
None-Steering automotive projects

## Slide 15: Nexteer Technologies Roadmap to Highly Automated Driving
Basic EPS
2000 2020 20xx
Low Speed Strg Position Control
Driver Override & Takeover
Steering Feel Dynamic Modulation
Input/Output Torque Overlay
AUTOSAR
State of Health Monitoring
Hands On/Off Wheel Detect
Fail Operational HW/SW
Auto Parking Assist
Vehicle Stability Assist
Lane Departure Warning
HW Vibration Alert
Overlay Arbitration
Traffic Jam Assist
Under- / Over-Steer Assist
Cyber-security Features
High-speed Position Tracking
ISO26262 Safety Architecture
Flying Cars

Trailer Backup Assist
Steer-by-Wire
Enhanced Steering HMI Interfaces
Road Surface Detection
Driver Monitoring
Lane Keeping Assist
Embedded Black Box OEM Functions
Vehicle Features
Nexteer Technologies
LEGEND
Quadrasteer
Lane Change Assist
Level 2 Highway Driving
Level 3 Highway Driving
Level 4 Highway Driving
Level 4 City Driving
Level 5 / Driverless Cars
Notes: 1999: Basic EPS
2002: Quadrasteer on GM Pickups – First steer-by Wire
2007: Automatic Parking on Ford Escape
2008: DSR for vehicle stability on Ford Mondeo / Fiat ?
2018: Cybersecurity : Secure Diagnostics, Secure Lock, Secure Programming. etc.

## Slide 16: ADAS & Autonomous driving roadmap Loss of assist mitigation : motivation
Core EPS assist function
  Sudden transition to the LoA state may be uncomfortable and have a startle effect on the driver
  The increased steering effort associated with LoA may result in incorrect driver perception that the vehicle is not steerable
  Some applications are assigning an ASIL rating to Loss of Assist
ADAS and Autonomous Driving functions
  Functions such lane centering, collision avoidance, autonomous driving, etc. may not rapidly terminated in the event of a fault until the driver has taken over the task
  Reverting to manual steering may not be an acceptable safe state with ASIL rating assigned

## Slide 17
No-Automation (Level 0) – driver is in complete control of the primary vehicle controls – brake, steering, throttle and motive power – at all times.
Function-Specific (Level 1) – automation at this level involves one or more specific control functions
Combination Function Automation (Level 2) – at least two primary control functions designed to work in unison to relieve driver
Limited Self-Driving Automation (Level 3) – driver is expected to be available for occasional control, but with sufficiently comfortable transition time
Full Self-Driving Automation (Level 4) – driver expected not to be available at any time during trip
ADAS & Autonomous driving roadmap NHTSA Proposed Levels
Notes: DELETE?

## Slide 18: ADAS & Autonomous driving roadmap Loss of assist mitigation : Possible solutions
LoA
NO LoA
Fault
Full Assist Performance
Reduced Assist Performance
Shutdown
“Limp Home”
Ramp Out
Immediate Off
“Limp Aside”
Other Reduced Functionality (Non-Assist)
Reduced Occurrence Rate / Full Functionality
Component & Rating Selection
Hardware Redundancy
Software / Diagnostics Design
Mech Design / Mfg & Quality Processes
Med/High performance SW backup function
Low performance SW backup function
No backup, but ramping capable
No backup or ramping available
Diagnostics Robustness
Chart: Failure Rate
| 0.0 | 10.0 | 10.0 | 100.0
Faulted Performance (Inverse) | 1 | 1 | 3 | 3
Acceptable Solutions
Minimum Fault Severity Requirement
Failure Rate Requirement
Current Design
Future Design
Reduce occurrence rate or reduce fault severity

## Slide 19: ADAS & Autonomous driving roadmap Loss of assist mitigation : HW & SW solution sets
Decreasing Severity with Fault Present
1V5

## Slide 20: ADAS & Autonomous driving roadmap Loss of assist mitigation : Progressive improvement of FIT
Chart: FIT Rate
| Baseline | A-0 | A-P | A-TP | A-TPF | B-TP | B-TPF | F-0 | F-B
 | 820 | 510 | 430 | 440 | 310 | 280 | 160 | 30 | 0

## Slide 21: ADAS & Autonomous driving roadmap Loss of assist mitigation : Fully populated LoA-mitigation MPP
Construction remains fully consistent with Nexteer MPP Bill of Process
Notes: Which type of system is this?

## Slide 22: ADAS & Autonomous driving roadmap Loss of assist mitigation : Technology examples

## Slide 23: ADAS & Autonomous driving roadmap Selected enabling steering technologies

## Slide 24: ADAS & Autonomous driving roadmap Steer-by-wire : Background & Current state
10 years since last Nexteer SBW project (joint project with BMW)
Decision in 2014 to initiate new SbW project
What is different since last projects:
  LOA countermeasures / Fail Operational building blocks available
  Many common control functions with Close Loop Steering Control
  Other needed features available – ex. Potentially use Simulated Travel Stops for hand wheel actuator
  Dual power source available on subset of vehicles
  Electronics cost on a downward trend
  ADAS Features Evolution
Building functional prototype with available production components
  REPS for road wheel actuator
  CEPS for hand wheel actuator
Develop in phases:
  1st focus on base steering functions
  2nd explore new features enabled with extra degree of freedom
Will develop production intent design concept in parallel
  Safety architecture
  Optimized component sizing, mechanical functional content

## Slide 25: ADAS & Autonomous driving roadmap Steer-by-wire : Development vehicle
REPS Gear for Vehicle Steering
CEPS Column for Gear Inputs and Steering Feel
No I-shaft Required
Notes: Modified - title

## Slide 26: N. Champetier visit – Saginaw Technical roadmap & Innovation Content
Our approach to innovation
EPS building block roadmap
ADAS & Autonomous driving roadmap
Non-Steering automotive projects

## Slide 27
ADAS & Autonomous driving roadmap Non-Steering automotive projects : Electric Brake Booster

## Slide 28
ADAS & Autonomous driving roadmap Non-Steering automotive projects : Electric Cooling Pump